## Slide 1
EMMERA
East Med Cross-border Marine
Environmental Risk Assessment
Data Collection and Analysis Report
Visual redesign | 2016–2024 evidence atlas

## Slide 2
EMMERA
Marine pollution signals: natural context + human pressure
Natural sources
Anthropogenic sources
The assessment separates background variability from pollution linked to maritime activity, ports, coastal infrastructure and other human drivers.
East Med Cross-border Marine Environmental Risk Assessment
01

## Slide 3
EMMERA
Methodology: gridded spatial assessment
A common polygonal grid converts heterogeneous observations into comparable spatial units for risk mapping and cross-port analysis.
1
Define AOIs
Bound the port, coastal zone and adjacent waters.
2
Digitize events
Translate incidents and satellite detections to grid polygons.
3
Aggregate metrics
Summarize size, frequency and pollution source.
4
Build atlas
Produce comparable hotspot maps for East Med ports.
East Med Cross-border Marine Environmental Risk Assessment
02

## Slide 4
EMMERA
Data collection methodology: evidence stack
Free open data
REMPEC and public incident records
Public authorities
Port partners and local marine authorities
Sentinel-1/2
Radar and optical satellite observations
GIS + statistics
Polygonal grids, spatial aggregation and analysis
Integrated workflow
Data ingestion → anomaly detection → GIS gridding → statistical summaries → pollution atlas
East Med Cross-border Marine Environmental Risk Assessment
03

## Slide 5
EMMERA
Data sources used for the East Med assessment
REMPEC 1982–2022
Sentinel-2 optical
Sentinel-1 radar
Local marine environment authorities complete the record with verified, port-specific information.
East Med Cross-border Marine Environmental Risk Assessment
04

## Slide 6
EMMERA
Data collection process: from observations to analysis
1
Define AOIs
Port boundaries and adjacent marine zones.
2
Detect anomalies
Satellite screening for potential pollution signatures.
3
Collect partner data
Compile incidents from port and environment partners.
4
Create GIS polygons
Digitize affected cells and observation footprints.
5
Run statistics
Aggregate size, frequency and source by port.
East Med Cross-border Marine Environmental Risk Assessment
05

## Slide 7
EMMERA
Ports analyzed: three AOIs across the East Mediterranean
3
ports analyzed: Haifa, Limassol and Eleusis
1,000+
Sentinel-1 and Sentinel-2 scenes screened
Atlas
pollution maps for hotspot identification
East Med Cross-border Marine Environmental Risk Assessment
06

## Slide 8
EMMERA
Source of pollution: satellite detections + partner records
Key findings
• Hotspots appear near port entrances, discharge points and dense vessel activity. • Pollution sources differ by port, requiring port-specific risk controls. • Gridded outputs make events comparable across jurisdictions and years.
Output: atlas of pollution maps with size, frequency and source layers
East Med Cross-border Marine Environmental Risk Assessment
07

## Slide 9
EMMERA
Limassol digitized pollution, 2016–2024
Spill size
Frequency
Source
Dominant cumulative source: Coastal (0.89 km²)
East Med Cross-border Marine Environmental Risk Assessment
08

## Slide 10
EMMERA
Haifa digitized pollution, 2016–2024
Spill size
Frequency
Source
Dominant cumulative source: Vessel (7.79 km²)
East Med Cross-border Marine Environmental Risk Assessment
09

## Slide 11
EMMERA
Eleusis digitized pollution, 2016–2024
Spill size
Frequency
Source
East Med Cross-border Marine Environmental Risk Assessment
10

## Slide 12
EMMERA
Cumulative polluted area by port
Chart: 
| Limassol | Haifa | Eleusis
Cumulative area km² | 2.33 | 9.3 | 7.07
Interpretation
• Haifa shows the largest cumulative affected area in the digitized dataset. • Vessel-related sources dominate Haifa and Eleusis. • Limassol is more balanced, with coastal sources slightly leading.
East Med Cross-border Marine Environmental Risk Assessment
11

## Slide 13
EMMERA
Limassol source profile: cumulative polluted area
Area by source (km²)
Chart: 
| Aquaculture | Coastal | Rig platform | Unknown | Vessel
Area | 0.57 | 0.89 | 0.2 | 0.17 | 0.5
2.33 km²
total cumulative polluted area
East Med Cross-border Marine Environmental Risk Assessment
12

## Slide 14
EMMERA
Haifa source profile: cumulative polluted area
Area by source (km²)
Chart: 
| Coastal | Navy | Unknown | Vessel
Area | 0 | 0.11 | 1.4 | 7.79
East Med Cross-border Marine Environmental Risk Assessment
13

## Slide 15
EMMERA
Eleusis source profile: cumulative polluted area
Area by source (km²)
Chart: 
| Coastal | Infrastructure | Unknown | Vessel
Area | 0.93 | 0.91 | 1.55 | 3.68
East Med Cross-border Marine Environmental Risk Assessment
14

## Slide 16
EMMERA
Overall pollution: comparative atlas and next steps
Eleusis
Haifa
Limassol
Recommended next step: convert the atlas into a repeatable risk dashboard with automated satellite ingestion, partner validation and periodic hotspot updates.
East Med Cross-border Marine Environmental Risk Assessment
15
Funded by the European Union. Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the European Union or the European Commission. Neither the European Union nor the European Commission can be held responsible for them.